## Slide 1
Motion or planning node
Topic:
/arm_controller/joint_trajectory
JointTrajectory (msg)
arm_controller
gripper_controller
joint_state_broadcaster
Action:
/arm_controller/follow_joint_trajectory
control_msgs/action/FollowJointTrajectory (type)
read()
/joint_states (topic)
sensor_msgs/msg/JointState
ros2_control Controllers
  managed by controller_manager:
ros2_control command interfaces
COMMAND PATH
write()
Gazebo joints
ros2_control state interfaces
Instantaneous joint position command
Gazebo hardware interface (GazeboSimSystem)
STATE / FEEDBACK PATH

## Slide 2
Motion or planning node
Topic:
/arm_controller/joint_trajectory
trajectory_msgs/msg/JointTrajectory
serial_trajectory_bridge_node
/joint_states (topic)
sensor_msgs/msg/JointState
ros2_control Controllers
Custom ROS 2 driver
ros2_control command interfaces
COMMAND PATH
Servo.write()
Physical robot joints
Instantaneous joint position commands
hardware interface
Custom hardware interface: Serial communication + Arduino firmware + SG90 servos
STATE / FEEDBACK PATH
• receives JointTrajectory
• schedules trajectory points
• converts radians → servo degrees
• applies calibration and limits
• sends serial commands
Publishes: sensor_msgs/msg/JointState (last commanded positions)

## Slide 3
MoveIt or motion node
scaled_joint_trajectory_controller
gripper_controller
joint_state_broadcaster
Action:
/scaled_joint_trajectory_controller/follow_joint_trajectory
control_msgs/action/FollowJointTrajectory (type)
read()
/joint_states (topic)
sensor_msgs/msg/JointState
ros2_control Controllers
  managed by controller_manager:
ros2_control command interfaces
COMMAND PATH
write()
Robot joints
ros2_control state interfaces
Instantaneous joint position command
UR hardware interface
UR ros2_control hardware interface
UR driver communication (RTDE)
UR controller box
STATE / FEEDBACK PATH
Measured joint positions (and velocities)
Joint encoders